## Slide 1: Inundation – Time Series Workshop Flanders
Sebastiaan Verbesselt
Habitats pilot meeting - 10/06/2025 – Diest, Belgium

## Slide 2: Study sites

## Slide 3: Study sites
Schulensbroek
Webbekoms Broek
Kloosterbeemden

## Slide 4: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
         already done for you (01/01/2020 – now)
        Available bands: B02, B03, B04, B05, B08, B8A, B11, B12, SCL

## Slide 5: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
    a. the boundary of your study area (AOI)
    b. the datacube
    c. wms layers of ortho imagery + DTM (background layers)
    d. Tytti’s model
    e. reference points taken in the field

## Slide 6: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
Data pre-processing:
    a. removal of trees
    b. explore historical ortho images of the area
    c. preprocess the datacube
    i. cloud and shadow masking
    ii. regional masking
    iii. calculate vegetation indices per pixel for the classification
    iv. check radiometric offset

## Slide 7: Question 1: which cloud cover threshold should we use? We now use a 5% threshold.

## Slide 8: Question 1: which cloud cover threshold should we use? We now use a 5% threshold.
We often use a 10 or 20% cloud cover threshold.
 | 5% cloud cover threshold | 10% cloud cover threshold | 20% cloud cover threshold
Number of observations | 145 | 155 | 172
% of the total number of observations (853) | 17% | 18% | 20%
Notes: Simuleer een resultaat

## Slide 9: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
Data pre-processing:
Classification (Jussila + Wiw models)

## Slide 12: Question 2: can you already spot some differences between the two models?

## Slide 13: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
Data pre-processing:
Classification (Jussila + Wiw models)
Visualize output of the last available date (Sentinel-2 image)
            a. check the classification output
            b. check the soil moisture/wetness indices
             compare with the GPS data points form the terrain

## Slide 14: Question 3: what can we conclude based form the last available Sentinel-2 image data? Does it match with our observations in the field?

## Slide 15: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
Data pre-processing:
Classification (Jussila + Wiw models)
Visualize output of the last available date (Sentinel-2 image)
Time series indicator analysis

## Slide 16: Overview analysis workflow
Download a time series datacube of Sentinel-2 images for the study area (Hans’s script) in OpenEO.
Load the datasets:
Data pre-processing:
Classification (Jussila + Wiw models)
Visualize output of the last available date (Sentinel-2 image)
Time series indicator analysis

## Slide 17: Time series indicator analysis
  Pixel level
  AOI level
  …
Decide spatial detail
  Spatial
  Temporal
GAP filling
  Spatial
  Temporal
Define indicator set
Decide temporal detail

## Slide 18: Time series indicator analysis
Decide temporal detail
  Pixel level
  AOI level
Decide spatial detail
  Spatial
  Temporal
GAP filling
  Spatial
  Temporal
Define indicator set
Inundated vs non-inudated (classification result)
(We did this already for the last available date)
Band value (like B11) or moisture/wetness index (e.g. NDMI, STR)

## Slide 19
STR – shortwave-infrared transformed reflectance index.

## Slide 20: Time series indicator analysis
Decide temporal detail
  Pixel level
  AOI level
Decide spatial detail
  Spatial
  Temporal
GAP filling
  Spatial
  Temporal
Define indicator set
Inundated vs non-inudated (classification result)
Band value (like B11) or moisture/wetness index (e.g. NDMI)
% of inundation (classification result)
Spatial statistics on band value (like B11) or moisture/wetness index (e.g. NDMI)
                * Central estimate: mean, median,…
                * Variance estimate: CV, std, variance, range, IQR,…
                * (Extreme estimate: min., max.)

## Slide 21: Question 4: in which case would we want to monitor on pixel level / on plot level?

## Slide 22: Question 4: in which case would we want to monitor on pixel level / on plot level?
Pixel level: when we want to keep spatial information, e.g. when your plot/area delineates a heterogenous habitat.
Plot level: when spatial information within your area is not required.

## Slide 23: Evaluation on plot level: % inundated (Jussila model)

## Slide 24: Evaluation on plot level: mean STR + sd (error bars)

## Slide 25: Time series indicator analysis
  Pixel level
  AOI level
Decide spatial detail
  Spatial
  Temporal
GAP filling
  Spatial
  Temporal
Define indicator set
Decide temporal detail

## Slide 26: Warning
Next few slides can become technical.
If you feel confused or dizzy. Don't panic, the presenter is also confused.
We will try summary the main conclusions and give concrete examples.

## Slide 27: Problems with our datacube

## Slide 28: Spatial gaps
Missing values due to cloud masking

## Slide 29: Temporal gaps
Revisit time of Sentinel-2  5 days (2/3 days for most places in Flanders)
?

## Slide 30: Evaluation on plot level: % inundated (Jussila model)
Time gap > 5 days (revisit time Sentinel-2).

## Slide 31: Evaluation on plot level: mean STR + sd (error bars)
Time gap > 5 days (revisit time Sentinel-2).

## Slide 32: Problem: How to deal with missing values (spatially, temporarely)?
Data fusion/prediction:
  E.g. Landsat - Sentinel-2 harmonized time series: https://hls.gsfc.nasa.gov/
  E.g. use Sentinel-1 data to predict values for Sentinel-2: https://blog.vito.be/remotesensing/cropsar2023
Lower the cloud cover threshold filter and rely on cloud masking (suboptimal)
Interpolation:
  Spatial versus temporal interpolation
  Which interpolation function should we use?
  On which spatial (pixel vs plot) and temporal level (e.g. 5 days vs 14 days)

## Slide 33: Spatial interpolation
Which value do you think this pixel would have?
?

## Slide 34: Spatial interpolation
Which value do you think this pixel would have?
E.g. spatial interpolation based on majority voting with 3x3 kernel
Many spatial interpolation techniques exists, like IDW, NN, ordinary Kriging,…

## Slide 35: Temporal interpolation
?

## Slide 43
Example of 6 different interpolation techniques for the % of inundation
(no temporal aggregation).
In my opinion:
Overfit:
Spline interpolation
Linear interpolation (prone to atmospheric conditions and errors of the models)
Kernel regression (but can give “steps” in the interpolation)
Underfit:
Loess regression
linear interpolation
Both over- and underfit:
Smoothing spline interpolation
 We still need to finetune the parameters in these interpolation techniques or use additional smoothing in case of overfitting. For seasonal events, you can use harmonic interpolation (but you can miss “rare” events).
More advanced interpolation technique (combines temporal interpolation, temporal smoothing and temporal aggregation):
https://pubmed.ncbi.nlm.nih.gov/39650555/

## Slide 44: Problem: How to deal with missing values (spatially, temporarely)?
Lower the cloud cover threshold filter and rely on cloud masking (suboptimal)
Data fusion/prediction:
  E.g. Landsat - Sentinel-2 harmonized time series: https://hls.gsfc.nasa.gov/
  E.g. use Sentinel-1 data to predict values for Sentinel-2: https://blog.vito.be/remotesensing/cropsar2023
Interpolation:
  Which interpolation function should we use?
  On which spatial (pixel vs plot) and temporal level (e.g. 5 days vs 14 days)
Temporal aggregation:

## Slide 45: Option 4: temporal aggregation
Choose a aggregation function:
  Pixel level:
    For classification output (0,1)
      Central estimates: Mode (Median here since mode does not work if freq. = 1 🡪 if case of equal frequencies = 0,5 (should be given a new class))
      Variance estimates: p * (1 – p) (with p the relative frequency of inundation)
      Extreme estimates: min, max
    Moisture/wetness indices
      Central estimates: mean, median,…
      Variance estimates: variance, std, CV, range, IQR,…
      Extreme estimates: min, max
  Plot level (% of inundation or moisture/wetness indices):
      Central estimates: mean, median,…
      Variance estimates: variance, std, CV, range, IQR,…
      Extreme estimates: min, max
Choose a time interval:
  10 days, 14 days (bi-weekly), 1 month, 3 months (season), 1 year,…

## Slide 46: Option 4: temporal aggregation
Choose a aggregation function:
  Pixel level:
    For classification output (0,1)
      Central estimates: Mode (Median here since mode does not work if freq. = 1 🡪 if case of equal frequencies = 0,5 (should be given a new class))
      Variance estimates: p * (1 – p) (with p the relative frequency of inundation)
      Extreme estimates: min, max
    Moisture/wetness indices
      Central estimates: mean, median,…
      Variance estimates: variance, std, CV, range, IQR,…
      Extreme estimates: min, max
  Plot level (% of inundation or moisture/wetness indices):
      Central estimates: mean, median,…
      Variance estimates: variance, std, CV, range, IQR,…
      Extreme estimates: min, max
Choose a time interval:
  10 days, 14 days (bi-weekly), 1 month, 3 months (season), 1 year,…

## Slide 47: Question 5: What are the advantages and disadvantages of using the min/max aggregation function on Tytti’s model (0: dry, 1: inundated). When would you use it?

## Slide 48: Question 5: What are the advantages and disadvantages of using the min/max aggregation function on Tytti’s model (0: dry, 1: inundated). When would you use it?
Advantages: detection of “rare” events (and keep the spatial information)
- e.g. in very dry areas where you want to detect inundation ,
or you want to detect complete drying of your area.
 max. aggregation.
- e.g. in very wet areas where you want to detect desiccation,
or you want to detect complete flooding of your area.
 min. aggregation
Disadvantage: sensitive to outliers (caused by problems in signal (atmosphere) or the model).
If you want more “smoothing” (general patterns)  use the mode (categorical) or median (on the numeric values of the categories (we handle categorical values as conitinous ones)).

## Slide 49: Example: pixel level, classification, max. aggregation
1. Monthly aggregation

## Slide 50: Example: pixel level, classification, median aggregation
1. Monthly aggregation

## Slide 51: If we would spatially aggregate (% inundated) for each month, what would be the difference?

## Slide 53: If we would spatially aggregate (% inundated) for each month, what would be the difference?
When still considering 0,5 and 1 as “discrete” pixels

## Slide 54
When still considering 0,5 and 1 as “discrete” pixels

## Slide 55
When still considering 0,5 and 1 as “continious” pixels

## Slide 56: But even after monthly aggregation of the pixel values, we still have spatial and temporal gaps…

## Slide 57: Larger timeblocks for aggregation is possible to create “regular” time series, but you loose information/relevancy…

## Slide 58: General problems/challenges with temporal aggregation

## Slide 59: Problem: How to deal with missing values (spatially, temporarely)?
Data fusion/prediction:
  E.g. Landsat - Sentinel-2 harmonized time series: https://hls.gsfc.nasa.gov/
  E.g. use Sentinel-1 data to predict values for Sentinel-2: https://blog.vito.be/remotesensing/cropsar2023
Lower the cloud cover threshold filter and rely on cloud masking (suboptimal)
Interpolation:
  Spatial versus temporal interpolation
  Which interpolation function should we use?
  On which spatial (pixel vs plot) and temporal level (e.g. 5 days vs 14 days)
Temporal aggregation:
Often, a combination of the gap filling methods results in the best solution

## Slide 60: But… in which order should I lay the puzzle?
Spatial inter-polation
Smoothing
Tempoal interpolation
Temporal aggregation
Again, depends on your case your interested.
Most common practice for general time series analysis:
1. Cloud mask
2. (optional small-gap spatial interpolation)
3. Temporal aggregation
4. Temporal interpolation/smoothing
However…
For general phenology / seasonal curve-fitting applications.

## Slide 61: Time series indicator analysis
  Pixel level
  AOI level
Decide spatial detail
  Spatial
  Temporal
GAP filling
  Spatial
  Temporal
Define indicator set
Decide temporal detail
When is there inundation?
Which area is inundated?
How much is the area inundated?
How long?
Changes in trend, seasonality,…

## Slide 62: E.g. Monitoring aapa mires by Titty
Pixel level
Decide spatial detail
Temporal aggregation, median
(2 weekly)
GAP filling
Temporal interpolation (linear)
GAP filling
  Spatial: pixel and plot level
  Temporal: year
Define indicator set
Temporal aggregation on (year level) on pixel level:
3 functions: min, max, mean
2. Spatial aggregation (plot level).
Plot scale:
Spatial average + range, visualized in a trend plot for soil/wentess indicators
Minimum and maximum range of inundated area 🡪 % wet, % dry, % seasonally
% of permanent dry, % seasonal and % permanetn wet pixels.

## Slide 63: Tytti’s indicators

## Slide 64: Tytti’s indicators

## Slide 65: Tytti’s indicators
In our area we have:
Permanent water bodies
Seasonally inundated grasslands
When the grassland are inundate too frequently or too long
 grassland degradation (loss in biodiversity)

## Slide 66: Adaptations to Tytti’s pipeline:
Pixel level
Decide spatial detail
Spatial aggregation, 3x3 kernel with majority voting
GAP filling
Temporal aggregation, median (per month)
GAP filling
Temporal interpolation (linear)
GAP filling
  Average inundation per pixel over a year.
  % permanent wet, dry and seasonally inundated
Define indicator set
+ uncertainty visualization:
    Spatial completeness per month: number of valid pixels
    Temporal completeness: % of valid months

## Slide 67: Adaptations to Tytti’s pipeline:
+ uncertainty visualization:
    Spatial completeness per month: number of valid pixels
    Temporal completeness: % of valid months
In white: the missing months
Legend: sum of valid pixels
 expected sum is between 5 and 6 (5 day revisit time), 9-10 (3 day revisit time)
       Clear under representation of winter months.

## Slide 68: Spatial gap filling

## Slide 69: Spatial gap filling

## Slide 70: Temporal aggregation (median value per month)

## Slide 71: Temporal interpolation (linear)

## Slide 72: Yearly indicators
Min, mean, max values taken over the monhtly time series
No zones that are permanently inundated, but the dynamics of seasonally inundation differs between years.